## Slide 1: 2D Quadrilateral FE Poisson and DG Advection Solvers for Plasma Simulation
Tal Rubin
May 2020

## Slide 2: Agenda
Motivation
Equations
Algorithms
Some Results

## Slide 3: Motivation
Plasma is a state of matter in which an ionized gaseous substance becomes highly electrically conductive to the point that long-range electric and magnetic fields dominate the behavior of the matter. [Wikipedia]
Full system of equations for the time evolution of plasma are the Maxwell-Vlasov equations.
  Vlasov -> distribution function, 6d phase space + time
Alternatively, taking moments of the Vlasov equation(s)
  0th moment: Continuity equation
  1st moment: Momentum equation
  2nd moment: Energy equation, and so forth
Fluid solvers are popular alternative to Vlasov Solvers
Coupled Fluid and Maxwell solvers

## Slide 4: Equations for this project
The Poisson equation and relates the difference between the electron set to zero here and ion densities to electric potential, which produces electric field.
The electric field appears on the right-hand-side of the momentum equation as a forcing term.
Most of the time ions are conserved.
1st Maxwell equation, 0th and 1st moments of Vlasov equation
Poisson equation:
  2D geometries could be complicated, its useful to be able to take spatial complexities into account.
Conservation equations:
  Stability issues, positivity and monotonicity preservation.

## Slide 5: Finite Element Solver for the Potential
The finite-element method is able to capture complex multidimensional geometry by dividing space into elements.
The elements implemented here are 2D quadrilaterals with 9 Lagrange nodes.
These element are deformable and can exactly match the boundaries of domains that can be locally parametrized by 2nd order polynomials.
The solution generated by these elements is composed of some of piecewise 2nd degree polynomials.
I used Dirichlet boundary conditions of grounded walls.
Quadrilateral Finite Elements
1
2
3
4
8
5
6
7
9

## Slide 6: Finite Element Solver for the Potential
For the differential equation:
An approximate solution in the form:
The residual:
Minimizing the projection of the residual on each test function:
Is equivalent to solving a system of linear equations:
Weak-Form formulation of PDE

## Slide 7: Finite Element Solver for the Potential
Its useful to have a uniform integral to solve, so a change of variables is made, with the vector N the vector of basis functions.
The stiffness matrix element becomes:
Or, using known functions:
Calculating the Integrals
Since this integral contains the inverse of a polynomial, it is evaluated by Gauss Quadrature.

## Slide 8: Finite Element Solver for the Potential
The stiffness matrix for each element for a regular grid.
Calculating the Integrals

## Slide 9: Finite Element Solver for the Potential
For F, we need the ion density, which is approximated using a different set of basis functions.
Since this time we have an integral of a polynomial we evaluate it analytically
For this I wrote a class that handles 2D polynomials analytically.
Since the potential quasi-static (under my assumptions), the matrices and are calculated only once.
Calculating the Integrals

## Slide 10: Finite Element Solver for the Potential
Polynomial2d
  Defines the class poly – handles analytically 2d polynomials
      Addition, multiplication, differentiation and integration, and representation in python and tex forms.
Quadratic_Poly_Functions
  Defines the basis functions for the elements
PreProc
  Pre-Processor, handles domain definition, division into elements, and matrix assembly.
  Returns a table of elements, list of node positions, stiffness and force matrices.
Solver
  Uses numpy to solve the linear system of equation.
Code structure

## Slide 11: Finite Element Solver for the Potential – Some Results
density
potential

## Slide 12: Discontinuous Galerkin Solver for Advection
Same steps as for FE:
With Legendre Polynomials basis functions.
Weak-Form formulation of PDE

## Slide 13: Discontinuous Galerkin Solver for Advection
Since we use quadratic functions in space, we need 3rd order RK in time:
Time solution

## Slide 14: Discontinuous Galerkin Solver for Advection
Calculating the Integrals
The flux matrix within each element:
The flux matrix out of the element:

## Slide 15: Discontinuous Galerkin Solver for Advection
Since the fluxes out of each side of the element generally don’t agree, we use a “numerical flux” to approximate the real flux.
The flux at each element boundary is set to be the average between the fluxes calculated for the solution in each side of the boundary.
Lax–Friedrichs numerical dissipation could be added.
Numerical Flux

## Slide 16
Questions?